## Slide 2: Chapter 4 Supplement Reliability

## Slide 3: Learning Objectives
Define reliability and compute the reliability of a product system.
Distinguish among the concepts of reliability, maintainability, and availability.

## Slide 4: Operations Profile: Computer Glitch Grounds United Airlines
On July 8, 2015, United Airlines suffered a computer failure of a network router that disrupted its reservation system.
United was forced to cancel 59 flights and delay over 800 flights due to the computer failure.
In a statement, United said that its network was reliable and includes a number of redundant systems, “but we continue to invest and improve on the reliability of those networks to deliver better service to our customers.”

## Slide 5: Understanding Reliability
Reliability can be defined as the probability that a component, product, or system can perform its intended function over a period of time under a given set of normal operating conditions of its use.
Because a product or system is made up of many components, the overall reliability of a product or system depends on the reliability of its individual components and the way in which they are arranged.

## Slide 6: Estimating Reliability
For a system to function properly, all of its individual components must also be working.
The overall reliability of that system is a product of the reliabilities of its individual components.
If there are n components in a system (S) with individual reliabilities of R (C1), R (C2), R (C3), etc., up to R (Cn) then the overall reliability of the system R (S) is given by:
R (S) = R (C1) x R (C2) x R (C3)….x R (Cn)

## Slide 7: Three Components Arranged in Series
If each component has a reliability of 0.95, then the overall reliability of the system R (S) is given by:
R (S) = R (C1) x R (C2) x R (C3) = 0.95 x 0.95 x 0.95 = 0.857
At any given time, when using the product, there is an 85.7% likelihood that the product will function correctly for a specified duration.

## Slide 8: Redundancy
To maintain or increase the reliability systems or products, the components or subsystems that perform the critical functions are often duplicated to serve as a backup if the original component or subsystem fails.
This duplication of critical components is called redundancy, by which duplicate systems operate in parallel to the original component.

## Slide 9: Three Components With Redundancy
Reliability of component 2 (original + backup):
R (C2) = R (OC2) + [1 - R (OC2)] x R (BC2) = 0.95 + (1- 0.95) x 0.90 = 0.995.
Reliability of the overall system:
R (S) = R (C1) x R (C2) x R (C3) = 0.95 x 0.995 x 0.95 = 0.898.

## Slide 10: Example 4S.1
An electrical power system has four major components with reliabilities of 0.99, 0.90, 0.95, and 0.96. All of the four components must function to prevent the failure of the electrical power system.
Compute the reliability of the overall power system.
If the designers of the system want to improve the reliability of the system by adding a backup component, which component should get the backup? Compute the reliability of the system with the addition of that component? Assume that the backup component has the same reliability as the original component.

## Slide 11: Example 4S.1 (Solution)
Compute the reliability of the overall power system.
P (S) = P (C1) x P (C2) x P (C3) x P (C4) = 0.99 x 0.90 x 0.95 x 0.96 = 0.8125
Since component 2 has the lowest reliability, it requires a redundant component as a backup.
Composite reliability of component 2 (+ backup):
P (C2) = P (OC2) + [1 - P (OC2)] x P (BC2) = 0.90 + (1- 0.90) x 0.90 = 0.99
Reliability of the overall system:
P (S) = P (C1) x P (C2) x P (C3) x P (C4) = 0.99 x 0.99 x 0.95 x 0.96 = 0.8938.

## Slide 12: MTBF
MTBF (mean time between failures) is the average time before the product or component fails.
For example, a car transmission may have a mean time of 5,000 hours between failures.
If your lawn mower fails five times in 200 hours of operation, then the failure rate of the lawn mower is 5/200 = 0.025, and its MTBF = 1/0.025 = 40 hours.
Manufacturers of new products can develop MTBF measures through intensive product testing.

## Slide 13: Availability and Maintainability
Availability is the percentage of the time that a system is operating properly when it is needed.
When a system or equipment has availability, it does not necessarily mean that it also has high reliability.
Reliability only considers the time it takes for a component to fail, but it does not take into account any downtime associated with the repairs.
Availability is not only related to reliability, but it is also a function of maintainability.
Maintainability is the ease with which an equipment or system can be repaired or serviced.

## Slide 14: Relationships Among Reliability, Maintainability, and Availability
Used with permission from ReliaSoft. Retrieved from http://www.reliasoft.com

## Slide 15: Example 4S.2
A laser printer is able to operate 300 hours between repairs, and the mean time to repair the printer is three hours. Compute the availability of the printer.
Given: MTBF = 300 hours; MTTR = 3 hours
Availability = MTBF/(MTBF+MTTR) = 300/(300 +3 ) = 300/303 = 0.99%
As the MTBF increases (reliability increases) and MTTR decreases (maintainability increases), availability also increases.