## Slide 2: Chapter 6: Quality Improvement and Control Tools

## Slide 3: Learning Objectives
Explain the difference between of quality control and quality assurance.
Apply the various tools for appraising the quality of products and processes.
Apply the various tools for preventing defects in products and processes, including control charts, a process capability analysis, and how to calculate Six Sigma levels of quality
Use quality design tools to improve product or process design.

## Slide 4: Operations Profile: Using Technology to Improve the Quality of Helicopter Rescue
In order to address the challenges of air rescue and improve the quality of its services, Air Methods, the country’s largest operator of emergency medical helicopters, has become the first to create an all-weather fleet able to routinely use satellite data.
Improved weather satellites and better communications made it easier for Air Methods to argue that rather than investing in expensive radar systems, satellite displays would be just as effective in allowing crews to avoid severe weather or areas of dangerously low visibility.

## Slide 5: Quality Control Versus Quality Assurance
Quality control is concerned with the quality of a product or service after it is produced or delivered.
By contrast, quality assurance (QA) is a set of procedures to improve a product or service’s quality before it is delivered.

## Slide 6: Quality Appraisal Tools: Check Sheet
Check sheets, which are useful for manufacturing processes and operations that are repeated, are forms used to collect and record quality-related data.

## Slide 7: Quality Appraisal Tools: Histograms
A histogram can be used to show the distribution of a set of quality-related data.
A histogram is a vertical bar chart that shows the frequency of occurrences of values.

## Slide 8: Quality Appraisal Tools: Pareto Charts
A Pareto chart is also a vertical bar chart.
However, unlike in a histogram, the bars are arranged in decreasing height from left to right.

## Slide 9: Quality Appraisal Tools: Scatter Diagrams
A scatter diagram is a tool that can be used to visually determine if two variables are related or correlated.
It can show whether changes in one quality variable have an influence on another quality variable.

## Slide 10: Quality Appraisal Tools: Fishbone Diagrams
A cause-and-effect diagram (also known as a fishbone diagram because of the way it looks) is a quality control tool that identifies, sorts, and graphically displays the potential causes of a quality problem.

## Slide 11: Quality Appraisal Tools: Process Flowcharts
A process flowchart graphically displays the steps in a manufacturing process and its flow.
Before beginning any process quality improvement effort, it is a good idea to represent the process in its current state using a flowchart.

## Slide 12: Statistical Process Control (SPC)
Statistical process control (SPC) uses statistical methods to monitor a process to determine whether it is stable and producing a product that conforms to specifications.
Attributes are characteristics that are counted using whole numbers and often categorized using either/or measures such as good or bad, whole or broken, defective or non-defective, and so forth.
Variables are quality characteristics that are measured on a continuous, or incremental, scale.

## Slide 13: Control Charts
A control chart is graph that shows whether a process has remained stable or has undergone some change over time.
A statistical process control chart has three features:
  A center line (CL), which represents the target value of the quality characteristic the firm is trying to achieve.
  An upper control limit (UCL), which represents the upper-limit value of variation in the process.
  A lower control limit (LCL), which represents the lower-limit value of variation in the process.

## Slide 14: Designing Control Charts
For designing a control chart samples are used because measuring every product or service produced is time consuming and costly.
The most frequently made assumption is that the sample values are normally distributed.
µ +1σ  68.3%
µ + 2σ  95.5%
µ + 3σ  99.7%
Upper control limit (UCL) = µ + 3σ, and the
Lower control limit (LCL) = µ - 3σ

## Slide 15: Design of Control Limits Based on the Normal Distribution

## Slide 16: Design of Control Limits Based on the Normal Distribution (Cont’d)

## Slide 17: When Is a Process in Control?
Given 3σ control limits, all sample data plotted fall within the control limits.
The plotted points are clustered around the center line and are randomly distributed and have no discernible pattern.
An approximately equal number of plotted points fall above and below the centerline.
There are no runs of 8 successive points on either side of the center line.

## Slide 18: When Is a Process in Control? (Cont’d)
Two out of 3 successive points do not fall within zone C.
Four out of 5 consecutive points do not fall within zone C, zone B, or both.
Fifteen consecutive points are not within zone A

## Slide 19: Constructing a Mean Chart
Step 1. Calculate the mean of each sample (x̅i)
Step 2. If the mean (µ) and standard deviation (σ) of the population are not known, calculate the grand mean (average of all the sample means).
Step 3. Calculate the standard error of the mean (σx̅) using σx̅ = σ / √n. If the standard deviation (σ) of the population is known. Otherwise, go to step 6.
Step 4. Calculate center line, upper and lower control limits using the following formulas:

## Slide 20: Constructing a Mean Chart (Cont’d)
Step 5. If the standard deviation (σ) of the population is not known, use the range value:
a. Calculate the mean (or average) of the ranges
b. Calculate the upper and lower control limits for the mean chart using A2 values from Table 6-1:
Step 6. Plot the sample means (along the y-axis) over the time periods (along the x-axis).
Step 7. Determine if the process is in control

## Slide 21: Example 6.1
A filling machine in a soft drink bottling plant is used to fill 16-ounce bottles of cola. The output of this process is normally distributed with a mean (µ) of 16 ounces and a standard deviation (σ) of 1 ounce. Quality control personnel monitor the filling process by checking independent samples of 25 bottles every hour.
  a. Construct a mean chart for this process
  b. During an eight-hour day the following sample means were obtained (in ounces): 16.05, 16.1, 15.94, 16.2, 15.95, 15.9, 16.05, and 15.93. Is there any evidence that the process is out of control?

## Slide 22: Example 6.1
Steps 1 and 2: The sample means, the mean (16 ounces) and the standard deviation (1) is given. So we skip step 1 and 2.
Step 3: Because know the standard deviation (σ =1 ounce) and the size of the sample (n = 25), we can compute the standard error of the mean using the following formula:
Step 4:
Step 5: Skip as we know (µ) and (σ) of the output
Step 6: Graph the mean chart (Next Slide)
Step 7: No rules violated, the process is assumed to be in control. No intervention is necessary at this time.

## Slide 23: Example 6.1, Solution

## Slide 24: Constructing a Range Chart
Step 1: Calculate the range for each sample
Step 2: Calculate the average of the ranges
Step 3: Calculate the center line and the upper and lower control limits for the range chart using:
Step 4: Graph the range chart, by plotting the sample ranges relative to the over the time periods
Step 5: Determine if the process is in control. If not, take the necessary corrective action to bring the process back in control.

## Slide 25: Control Charts for Attributes: C-Charts and P-Charts
The two most common types of attribute control charts are c-charts and p-charts.
C-charts are used to monitor countable occurrences, such as the number of non-conformities or defects per unit. The unit can be a unit of a product, a unit of time, a unit of area, a unit of volume, and so forth.
P-charts are used to monitor the fraction, or proportion, of defects or errors in a product or service.
In general, control charts for attributes, unlike variables, require larger sample sizes to develop meaningful quality measures.

## Slide 26: Constructing a C-Chart
Step 1: Ensure that the data to be collected meets the assumptions of a Poisson distribution.
Step 2: Decide on the data collection frequency
Step 3: Compute the process average or mean:
Step 4: Compute the upper and lower control limits:
Step 5: Plot the number of defects for each sample.
Step 6: Interpret the chart to see if the process is in control by checking for special cause variations such as points beyond the control limits.

## Slide 27: Example 6.4
King’s Court Hotel, in its ongoing efforts to improve its service to its guests, is planning to develop a c-chart to monitor the number of customer complaints it receives each day. The data collected is assumed to have come from a population that has an underlying Poisson distribution. Additionally, the sample data collected is large enough to assume it is normally distributed.
Data on customer complaints for 20 days were collected and are given in the next slide.

## Slide 28: Example 6.4 (Cont’d)
Construct a c-chart for this hotel example using 3σ upper and lower limits.
Is this process in control?

## Slide 29: Example 6.4 (Cont’d)
Step 1: Poison distribution assumptions are met.
Step 2: All sampling requirements have been met.
Step 3: Compute the process average:
Step 4: Compute the upper and lower control limits:
Step 5: Draw the control chart (Next Slide)
The process appears to be in control because none of the plotted points fall outside of the control limits. In addition, there does not appear to be any pattern to the variation.

## Slide 30: Example 6.4 (Cont’d)

## Slide 31: Constructing a P-Chart
Step 1: Ensure that data are from a binomial population and the sample size is large enough.
Step 2: Choose a large sample size (n) and the number of samples (k) to be collected.
Record the number of defective units, and calculate the proportion of them for each sample.
Step 3: Compute the average of proportion of defective units (p̅) in the samples:

## Slide 32: Constructing a P-Chart (Cont’d)
Step 4: Compute the upper and lower control limits:
Step 5: Draw the control chart by graphing the center line and the upper and lower control limits. Plot the percentage of defective units
Step 6: Interpret the chart to see if the process is in control by checking for special cause variations.

## Slide 33: Example 6.5
The Good Will Tire Company in Jodhpur, India wants to construct a p-chart to monitor the quality of tires it manufactures. In order to collect data for the chart, the quality control manager of the company uses a sample size of 100, and records the number of defective tires and non-defective tires on a daily basis. The number of defective tires recorded for 20 samples is shown in the next slide.
Assume that the distribution of the total output is binomial and n × p ≥ 5.
a. Construct a p-chart for this example using 3σ control limits.
b. Is this process in control?

## Slide 34: Example 6.5 (Cont’d)

## Slide 35: Example 6.5 (Cont’d)
Step 1: Assumptions are met.
Step 2: Sample size and defective items are given.
Step 3: Compute the average proportion of defective:
Step 4: Compute the upper and lower control limits:
Step 5: Plot the percentage of defective (Next Slide)
Step 6: The chart shows that the process appears to be in control.

## Slide 36: Example 6.5 (Cont’d)

## Slide 37: Process Capability Analysis
SOURCE: Kapadia, M., (n.d.), http://www.symphonytech.com/articles/pdfs/processcapability.pdf

## Slide 38: The Process Capability Index (Cp)
The process capability index (Cp) is a measure of how well a process meets its specification limits.
Process variability is typically set at 6σ. Therefore:
If Cp is less than 1, process is not capable of consistently meeting its design specifications.
If Cp is greater than 1, process is always capable of meeting its design specifications.

## Slide 39: Example 6.6
A company manufactures piston rings for automotive companies. Design specifications require the diameter of the piston rings to have a target value of 75mm with a tolerance of 0.5mm. The current manufacturing process produces pistons rings with an average diameter of 74.8mm and a standard deviation (σ) of 0.15mm.
Is the company’s manufacturing process capable of meeting design specifications?

## Slide 40: Example 6.6 (Cont’d)
With a target value of 75mm and a tolerance of 0.5mm, the design specification limits are 75.5mm and 74.5mm. Therefore:
The process capability index of 1.11 indicates that the company’s manufacturing process is capable of meeting the design specifications.

## Slide 41: The Process Centering Capability Index (Cpk)
The process capability index (Cp) is the primary measure used to track process capability.
The formula for the Cpk is:
In cases where the process is off center we can apply a correction factor (K) to the Cp.

## Slide 42: Example 6.7
Refer to example 6.6. Compute Cpk and the off-center correction factor K.
Solution:
From example 6.6, USL = 75.5mm; LSL = 74.5mm; mean = 74.8mm and D = (75.5+74.5)/2 = 0.75.
Using the formula for Cpk and K, we have
Cpk = Min [ ((74.8 – 74.5)/3 × 0.15), ((75.5 – 74.8)/ 3 × 0.15)] = Min [0.67, 1.55] = 0.67

## Slide 43: Revisiting Six Sigma: Calculating Six Sigma Quality of a Process

## Slide 44: Revisiting Six Sigma: Calculating Six Sigma Quality of a Process (Cont’d)
In order to calculate the Six Sigma level of any process, we can use the following equation.
The percentage of defects from the process can be calculated by using the following formula (MS Excel):

## Slide 45: Example 6.8
The customers of a pizza delivery shop expect their pizzas to be delivered within 20 to 30 minutes. In order to improve its customer service levels, the shop collected past data on delivery times and found that the average delivery time was 27 minutes with a standard deviation of 3 minutes. What is the Six Sigma quality level of this pizza delivery process and the percentage of late deliveries?

## Slide 46: Example 6.8 (Cont’d)
This means that pizza deliveries exceeded 30 minutes 16% of the time.

## Slide 47: The Taguchi Loss Function
When every quality characteristic of a product meets its target value, the loss is at a minimum.
Any deviation from the product’s quality characteristic target value results in losses, including loss to the society.
The losses associated with poor quality should be expressed in monetary units.

## Slide 48: Example 6.9
Crescent Inc. produces socket tools that have inside diameters with a target value of 0.5", and a tolerance of 0.050". The tools have been meeting the target value, although several of them were rejected at the assembly stage. Recently, a tool produced by the process did not meet its target value because it had an inside diameter of 0.550 inches. The failure costs associated with a defective socket tool is $50.00. Using the sample data (next slide) collected from a recent production lot and the Taguchi loss function formula, justify why replacing the equipment may benefit the company and the customer.

## Slide 49: Example 6.9 (Cont’d)

## Slide 50: Example 6.9 (Cont’d)
X̅ = 0.501 and s = 0.0215
The target value of the inside diameter T = 0.5
The measured inside diameter X = 0.550
The expected loss for a tool L(X) = $50.00
L(X) = k × (X – T)2
50 = k × (0.550 – 0.500)2
Therefore, k = 50/ (0.550 – 0.500)2 = 20,000. So, the average loss per socket tool in this sample is
L = k × (s2 + (X̅ - T)2) = 20,000 × [(0.0215)2 + (0.501 – 0.500)2] = 9.28, or $9.28.
Total loss = $9.28 × 50 = $464.

## Slide 51: Parameter Design
Factors that affect the design of any product:
Control factors are variables affecting a process that a designer can easily control.
Signal factors are input factors that are also controlled by the designer so that the product can perform its intended functions.
Noise factors are factors affecting a process that are difficult for a designer to control.

## Slide 52: Design of Experiments (DOE)
Design of experiments is a set of statistical techniques used to determine which controllable factors and which noise factors are the significant variables that will have an impact on product/process or system performance.
The purpose of using DOE is to come up with settings for the controllable factors at those levels that will make the product or process insensitive to the noise factors.