## Slide 2: Chapter 9: Supplement Tools for Analyzing, Designing, and Selecting Processes and Layouts

## Slide 3: Learning Objectives
Employ tools for process selection, analysis, and design
Describe and use the techniques for designing process and product layouts.

## Slide 4: Operations Profile: Relieving Congestion at St. Francis Hospital
Notes: Because of overcrowding and inefficient emergency department work flow layout, the average time for a patient’s length of stay was nearly 4 hours.
When a patient arrives, hospital staff needs to get both registration information and clinical information about the patient’s condition.
These problems and delays prompted low patient satisfaction evaluations, as well as poor door-to-bed times.
Looking for ways to improve this situation, the ED team at St. Francis Hospital set out to integrate their registration and clinical information processes.
Within one year of the implementation of this practice, St. Francis decreased their patients’ length of stay from 253 minutes to 173 minutes.
Also, the rate of patients who left without being seen decreased from 3.86% to 2.62%, – all during a period of increased ED volume.

## Slide 5: Process Selection, Design, and Analysis Tools
One of the simplest tools used to compare and select processes is a cost-volume, or breakeven, analysis.
We calculate the total costs of the processes we are considering for various production volumes.
We then plot the total cost lines for each process and choose the one that has the lowest cost for the number of units we expect to produce.
If the lines intersect, it indicates that the total costs of the processes are identical at a certain production volume.
The points of intersection: points of indifference.

## Slide 6: Example 9S.1
Dantzig Corporation would like to evaluate three production processes (A, B, and C) to accommodate the changes in demand for its products.
Determine the most cost-effective process for an expected annual production volume of 3,000 units.
Determine the production volumes at the points of indifference between these processes and the range of annual volumes of production at which each of three processes would become most economical.

## Slide 7: Example 9S.1 (Cont’d)
A) Total cost for A = 25,000 + (3,000 ×42) = $151,000
Total cost for B = 50,000 + (3,000×32) = $146,000
Total cost for C = 90,000 + (3,000×22) = $156,000
Process B seems to be the most economical process.
B) Volume where the costs of A and B are equal:
25,000+ (Q×42) = 50,000+ (Q×32)
Q×(42-32) = 50,000-25,000
10×Q = 25,000
Q = 2,500

## Slide 8: Example 9S.1 (Cont’d)
Volume where the costs of B and C are equal:
50,000 + (Q × 32) = 90,000 + (Q×22)
Q × (32-22) = 90,000-50,000
10×Q = 40,000
Q = 4,000

## Slide 9: Tools for Analyzing and Designing Processes Assembly Drawings
An assembly drawing is an enlarged view of a product that shows all of its parts and sub-assemblies.

## Slide 10: Assembly Chart
An assembly chart, which is sometimes called a Gozinto chart, maps how a product’s parts go together and the order in which they are assembled.

## Slide 11: Route Sheet
A route sheet is a document that describes the sequence of different operations, places, or people involved in a process.

## Slide 12: Process Charts
A process chart uses graphics to show all activities related to a process, including its inputs and outputs, decision points such as approvals and exceptions, and any cross-functional relationships.

## Slide 13: Process Charts (Cont’d)

## Slide 14: Value Stream Maps and Process Simulations
A value stream map (VSM) is a process-mapping technique used to analyze and design the flow of materials and information across multiple processes.
The charting and graphical techniques we have discussed so for in this supplement can only provide a static view of a process.
A process simulation, by contrast, can provide a dynamic view.
Using computers, multiple inputs, work centers, and processing techniques can help operations manager look at the variability of a process under different conditions.

## Slide 15: Tools for Analyzing Service Processes Service Blueprints
Service blueprints are especially useful for analyzing service processes that have high service content such as the intensive customer interaction observed in hotels.
SOURCE: Adapted from http://www.hotelmule.com/attachments/2010/01/26_2010010704581522KeF.jpg; accessed November 2012.

## Slide 16: Layout Analysis Tools: The Cost Minimization Method
The most common way to design a process layout (as well as a fixed layout) for a manufacturing facility is to arrange departments or work centers so that the total cost of materials handling is minimized.
The total cost of materials handling in manufacturing process layouts depends upon three factors:
  The cost of moving a load between departments.
  The number of loads to be moved between departments.
  The distance between departments.

## Slide 17: Example 9S.2
Design a process layout for a factory with six departments with the objective of minimizing the total cost of handling materials. The dimension of each department is 20 x 20 feet, and the building is 80 feet long and 60 feet wide. The cost of moving a load between each pair of departments is $1.
Develop a revised layout by eliminating nonadjacent moves between work centers with high interactions and compute the total cost.
Note: Departments diagonal to one another are considered to be adjacent.

## Slide 18: Example 9S.2 (Cont’d)

## Slide 19: Example 9S.2 (Cont’d)

## Slide 20: Example 9S.2 (Cont’d)

## Slide 21: Process Layout Analyses Using Qualitative Data: The Relationship Rating Method
The relationship rating technique developed by Richard Muther is a method used to design new layouts or change old ones based on qualitative criteria.
Managers rate the best locations for departments relative to one another, and the information is displayed in a grid known as Muther’s grid. Symbols or letters represent the relationships between departments.

## Slide 22: Technique for Designing Product Layouts Line Balancing
In a product layout, machines or work centers are arranged based upon a pre-determined sequence of operations for the product.
The goals are to achieve high levels of efficiency and capacity utilization while ensuring that the product flows smoothly through the line with no bottlenecks.
Cycle time is another constraint that can make it difficult to balance a line.
Cycle time is the time required for the line to produce one unit to achieve an output rate that allows a firm to meet its demand requirements.

## Slide 23: Line Balancing (Cont’d)

## Slide 24: Steps in Line Balancing

## Slide 25: Line Balancing (Cont’d)

## Slide 26: Example 9S.3
An assembly line to be balanced has 11 tasks with precedence relationships. The task times are shown in Table 9S.3. Based on demand forecasts for the product to be assembled in the line, management has decided on an output rate of 120 units per day. The line operates eight hours a day. Given this information, balance the assembly line using both the most-following-tasks rule and the ranked-positional-weight rule (see Table 9S.2).

## Slide 27: Example 9S.3 (Cont’d)

## Slide 28: Example 9S.3 (Cont’d)

## Slide 29: Example 9S.3 (Cont’d)

## Slide 30: Example 9S.3 (Cont’d)

## Slide 31: Example 9S.3 (Cont’d)

## Slide 32: Software for Designing Process Layouts
Typically real-life layout problems are large, complex, and require the use of software.
For large process layout problems that involve quantitative criteria such as cost minimization, a computer program called CRAFT, which is an acronym for Computerized Relative Allocation of Facilities Technique, can be used.
NOTE: The software program went through three iterations to achieve the best possible layout for a total cost reduction of ($20,100 – $14,390 = $5,710.
SOURCE: Reprinted from http://image.slidesharecdn.com/layout-1223621497671389-9/95/layout-21-728.jpg?cb=1223616922