## Slide 2: Chapter 18: Master Scheduling and Material Requirements Planning

## Slide 3: Learning Objectives
Compose a master schedule and identify its functions.
Explain the conditions under which MRP is appropriate, its inputs, processing, and output, as well as its benefits and limitations.
Discuss the role that sustainability and ethics play in MRP systems.

## Slide 4: Master Scheduling
Operational plans for the medium to short term of the planning hierarchy and are listed below:
  Master scheduling
  Material requirements planning
  Capacity requirements planning
  Detailed scheduling
These tasks follow a sequence that can be presented in the framework shown in Figure 18.1.

## Slide 5: Master Scheduling Inputs, Processing, and Outputs
The inputs to the master schedule are the beginning inventory levels of the product, forecasts of demand for each period of the master schedule planning time frame, and customer orders for each period of the schedule (quantities committed to customers).
There are various lot sizing techniques that can be used to determine production quantities in the master scheduling process.
The appropriate choice depends on the demand pattern for the specific product.

## Slide 6: Example 18.1
Prepare a master production schedule for the Just Plowing Company, a manufacturer of snow blowers. The demand forecast for these snow blowers for each week of an 8-week schedule is 60 units. The production lot size is 80 units and production is scheduled in those weeks when the projected on-hand inventory becomes negative (i.e., when there are shortages). In addition, the company has the following committed customer orders for the first 4 weeks: 65, 45, 30, 18. Assume a beginning inventory of five snow blowers. Construct a master schedule for the 8-week time horizon.

## Slide 7: Example 18.1 (Cont’d)

## Slide 8: Example 18.1 (Cont’d)

## Slide 9: Example 18.1 (Cont’d)

## Slide 10: Functions of the Master Schedule
Disaggregation of the Sales and Operations (Aggregate) Plans.
Evaluation of Capacity Requirements.
Generation of Material Requirements.
Facilitation of Information Processing.

## Slide 11: Master Schedule Planning Horizon and Replanning
The appropriate time intervals and planning horizons used in master scheduling are determined by the type, volume, and component lead times of the products being produced.
As the planning process progresses over time, customer orders are met and new demand information is generated, the master schedule needs to be updated.
This updating is done on a rolling schedule, where the impact of the actual transactions on the master schedule is captured from one period to the next.

## Slide 12: Achieving Master Schedule Stability
Companies with an effective master schedule use the process of time fencing to achieve this stability.
In the time fencing approach, the master schedule time horizon is divided into three portions: frozen time fence, slushy time fence, and flexible time fence.
The frozen time fence describes the portion of the master schedule in which no changes to the schedule can be accommodated unless a senior executive requests such changes.

## Slide 13: Material Requirements Planning (MRP)
MRP is vital for companies that produce finished products from purchased components.
Specifically, MRP determines:
  what components and materials are needed for the final products and the quantities required to produce, fabricate, or assemble those end items
  when (on what date) these components and materials should be ordered from an outside supplier or produced from an in-house production facility
Thus, the MRP system triggers the lower level requirements for components and materials.

## Slide 14: MRP Terminology
Gross requirements
Net requirements
Parent and component items
MRP explosion
Time phasing/Time buckets
Lead-time offset
Scheduled receipt
On-hand inventory
Lot-size
Planned order receipt
Planned order release

## Slide 15: MRP Terminology (Cont’d)

## Slide 16: The Master Schedule
The master production schedule (MPS) record specifies what end items are to be produced, in what quantities that are to be produced, and when they are needed.
The MPS quantities are calculated based on information from several sources, such as forecasts and customer orders for end products, warehouse orders, interplant orders, and safety stock requirements.
Given these inputs for end item requirements and their lead times, the MRP system converts these requirements into individual time-phased component and material requirements.

## Slide 17: The Bill of Materials File
A bill of materials (BOM) file is a computerized data file that contains the complete listing of all assemblies, subassemblies, parts and components, and raw materials needed and the manufacturing and assembly sequence to produce one unit of a finished product.

## Slide 18: The Bill of Materials File (Cont’d)

## Slide 19: Example 18.2
The final assembly of a chair requires a leg assembly, a seat, and a back assembly. Each leg assembly requires two legs and a cross bar. Each back assembly requires two side rails, one cross bar, and three back supports. Given this information:
  Construct a product structure tree for the chair using low-level coding
  Determine the quantities of assemblies and components that will be required to assemble 10 chairs, given the following on-hand inventory:
    Leg assemblies = 2; back assembly = 1; legs = 4; cross bars = 6; side rails = 4; back supports = 10

## Slide 20: Example 18.2 (Cont’d)

## Slide 21: Example 18.2 (Cont’d)

## Slide 22: The Inventory Status file
The third input to an MRP system is the inventory status file, which contains the records of all items in the inventory, including on-hand inventory and scheduled receipts.
The inventory status file also contains information about the supplier, lead times, and lot size policy for each item.
From the master production schedule and the BOM file, the MRP system will determine the gross component requirements of materials and components for each production level.

## Slide 23: MRP Process
The master production schedule provides information on the number of units required for an end-product for specific time periods of the planning horizon.
The MRP system accepts these end-product requirements from the master schedule and then gathers information from the BOM file on the components needed to assemble the end product.
The MRP system also accesses information on the available inventory for both finished products and the various components.

## Slide 24: Example 18.3
Suppose a firm producing wheelbarrows has customer orders with delivery due dates of 50 in week 1, 70 in week 4, 70 in week 6, and 40 in week 8. Refer back to Figure 18.4 for the product structure tree for a wheelbarrow. The product structure tree shows that the subassemblies required for each wheelbarrow are one handle bar assembly and one wheel assembly. Each wheel assembly requires one tire. Prepare a material requirements plan for the handle bar assemblies, wheel assemblies, and tires for an 8-week planning horizon.

## Slide 25: Example 18.3 (Cont’d)

## Slide 26: Example 18.3 (Cont’d)

## Slide 27: Example 18.3 (Cont’d)

## Slide 28: Example 18.3 (Cont’d)

## Slide 29: Example 18.3 (Cont’d)

## Slide 30: Example 18.3 (Cont’d)

## Slide 31: Example 18.3 (Cont’d)

## Slide 32: MRP Outputs
Planned Order Schedules: These schedules delineate the quantity and timing of future material orders.
Planned Order Releases: These reports authorize the execution of the planned orders.
Changes to Planned Orders: Changes to planned orders might include cancellations of orders or revisions of orders.
Performance Control Reports: These are reports that managers can use to track problems such as missed delivery dates and stock outs in order to evaluate MRP system performance.
Planning Reports: These reports can be used to forecast future inventory requirements.
Exception Reports: These reports call managers' attention to major problems such as overdue and late orders, excessive scrap rates, reporting errors, and requirements for nonexistent parts.

## Slide 33: Other Considerations in MRP
Changing the Planning Horizon and Re-planning of the MRP System: The MRP planning horizon can be 10, 26, or even 52 weeks.
Lead Times: The actual lead times are not always the same as the planned lead times.
Safety Stocks: If there is supply or demand, uncertainty and the expected cost of running out of stock is high, then businesses hold safety stock.
Lot-sizing Considerations: In MRP, purchase or shop orders must specify a discrete quantity (lot size) to purchase or produce.

## Slide 34: Potential Benefits and Drawbacks of MRP
Benefits of MRP systems:
  Inventory benefits
  Ability to track material requirements
  Capacity benefits
Drawbacks in using MRP systems:
  They are as good as the inputs they receive
  They can be difficult, time consuming, and costly to implement
  All employees who use the system should receive adequate training and education

## Slide 35: Integrating MRP and JIT Systems

## Slide 36: Integrating MRP and JIT Systems (Cont’d)
SOURCE: Ho, J. C., & Chang, Y. L. (2001). Integrated MRP and JIT framework. Computers & Industrial Engineering. 41:173–185.

## Slide 37: Features of Integrated MRP and JIT Systems
Just as in MRP systems, the system is triggered by the requirements for a higher-level parent item provided by the master schedule.
Similar to JIT systems, the demand for this parent item pulls or triggers the last operation for this item. To schedule operations such as this one, decision rules need to be embedded in the integrated system.
The scheduling of the last operation of this parent item triggers all preceding operations for the lower-level children of the parent item until all operations required to produce the parent item specified by the master schedule are scheduled.

## Slide 38: MRP in the Service Sector
MRP is useful for service companies or service items that have dependent demand.
Restaurants typically use MRP systems because the ingredients and side dishes for a meal such as vegetables, spices, meat, pasta, and bread are dependent demand items.

## Slide 39: MRP in the Service Sector (Cont’d)

## Slide 40: Ethical and Sustainability Issues in MRP
Government actions and pressure from investors and consumers have caused companies to reexamine their manufacturing and service operations in light of sustainability.
Government agencies enforce regulations on environmental conditions that affect manufacturing practices.
Investors are wary of the environmental liabilities of companies they are considering funding.
Consumers seek proof of environmental responsibility in the products and services they purchase.