## Slide 2: Chapter 19: Detailed Scheduling

## Slide 3: Learning Objectives
Define detailed scheduling
Demonstrate the main types of scheduling and show when each type should be employed.
Explain why scheduling is complex.
Describe the scheduling methods used in service organizations.
Describe supply chain scheduling.
Explain how companies can make scheduling decisions to promote sustainability.

## Slide 4: What Is Detailed Scheduling?
In the hierarchy of decisions made in the field of operations, detailed scheduling is the final step before the actual production of the product or delivery of the service.
Scheduling is the process of making specific resources such as labor, equipment, and facilities to produce a product or deliver a service available.

## Slide 5: Objectives of Scheduling
Managers have to balance several conflicting goals. Hence, the objectives of scheduling are to achieve the necessary tradeoffs among these goals to ensure that:
  Resources such as equipment, labor, and facilities are used effectively
  Productivity is increased by maximizing the flow of goods and services through the facility
  Customer waiting time, work-in-process inventories, processing times, and thus overall costs are minimized

## Slide 6: Types of Scheduling for Manufacturers (Line Process Scheduling)
Line processes are high-volume production processes that typically produce standardized products and require identical or similar operations.
The following steps should be used to schedule multiple products through a line flow process:
  Step 1: The key issue in scheduling is the changeover time in switching production
  Step 2: After determining lot size, the next step is to determine when each product should be produced
  Step 3: After calculating the run out times for each product, the next step is to schedule first one lot of that product that has the lowest runout time

## Slide 7: Intermittent Process Scheduling
In an intermittent process, a firm produces a variety of products in relatively low volumes.
In intermittent processes such as job shops, products are made to order and each order has its own unique material and processing requirements, processing sequence, and processing time.
Main problem here is how to manage the queues of work-in-process inventories that build up at each work center as jobs wait for these work centers.
To minimize the size of these queues, schedulers need to address the following three issues: Input-output control; loading; and sequencing.

## Slide 8: Input–Output Control
Input–output control is concerned with regulating inputs to a work center in relation to output and available capacity so that the queues and waiting times of jobs can be managed and kept under control.

## Slide 9: Loading
Loading is the assignment of jobs to work or processing centers.
Loading decisions are straightforward if a job can be processed exclusively in a specific work center.
Managers use tools such as Gantt charts or the assignment method to load work centers.

## Slide 10: Loading (Cont’d)

## Slide 11: The Assignment Method
The assignment method is a special case of a group of problems known as linear programming problems (LP).
Linear programming is a technique used to optimize an objective (such as maximizing profits or minimizing cost) under certain constraints, such as availability of resources.
The assignment method is applied to situations in which various resources must be allocated to activities on a one-to-one basis.

## Slide 12: Example 19.1
A factory supervisor has three workers available and three jobs to be completed. The supervisor has to decide which job should be given to which worker (load jobs). The table shows the costs incurred in performing each job by each worker. The supervisor wants make this assignment to minimize the total cost, under the constraint that only one job can be assigned to one worker.

## Slide 13: Example 19.1 (Cont’d)
Step 1: Row reductions.
Step2: Column reductions.
Step 3: Cross out the zeroes in the table by using minimum number of horizontal and/or vertical lines.
Step 4: Check for an optimum solution.
Step 5: Repeat Steps 3 and 4 until you get an optimum solution.
We needed three lines to cover all zeroes in this matrix. That number of lines equals the number of rows or columns, and an optimum solution has been reached. Thus, we assign Job A to Worker 3, Job B to Worker 2, and Job C to Worker 1.

## Slide 14: Backward and Forward Scheduling
Backward scheduling begins with the due date for each job and loads the processing requirements for these jobs at each work center by proceeding backward in time.
Forward scheduling begins with the current date for those jobs that have known processing requirements, and it loads the jobs forward in time.

## Slide 15: Loading Approach in Scheduling
At the CRP stage, infinite loading is the more appropriate approach to load the work centers.
At scheduling stage, however, in order to avoid exceeding capacity, the finite loading is the preferred approach because it takes into account the actual processing times of jobs and the available capacity at each work center.
By using the finite loading approach, managers can determine detailed schedules for each job through each work center based on available work center capacities and other jobs that have already been scheduled.

## Slide 16: Sequencing
Priority rules used for sequencing individual jobs:
  First Come, First Served
  Shortest Processing Time
  Earliest Due Date
  Longest Processing Time
  Critical Ratio (CR)
    If CR > 1 and the job is ahead of schedule
    If CR = 1 and the job is on schedule
    If CR < 1 and the job is behind schedule

## Slide 17: Priority Rules Assumptions
The set of jobs to be processed are known and do not change, i.e., existing jobs are not canceled and no new jobs arrive.
Setup times and processing times of jobs are known and do not vary.
Setup times are independent of job processing sequence.
There are no unexpected interruptions in job processing, such as machine breakdowns or accidents.

## Slide 18: Example 19.2
Susan Burke is the manager of a custom furniture job shop. She has five jobs, shown in the table, that are waiting to be processed through a work center. Susan is what the exact sequence of job processing should be. Help Susan to determine the exact sequence for processing these jobs, the average flow time, average job tardiness, and the average number of jobs in this work center, for each of the following priority rules and compare the relative performance of these priority rules for the three performance criteria. Assume that the jobs have arrived in the order shown in the table.

## Slide 19: Example 19.2 (Cont’d)
For Example 19.2, the SPT rule has the best performance because it has the lowest value for all three measures.
The ranking of the other priority rules is: EDD, FCFS, and LPT.

## Slide 20: Example 19.2 (Cont’d)

## Slide 21: Example 19.2 (Cont’d)

## Slide 22: Example 19.2 (Cont’d)

## Slide 23: Example 19.3
Blake Miller has five jobs waiting to be processed through his grinding and polishing work center. The due dates for these jobs and their remaining processing time in days are given in the table below. Suggest a sequence of job processing for the grinding and polishing work center using the critical ratio rule. Today is day 20.

## Slide 24: Example 19.3 (Cont’d)
Based on the critical ratios, the current sequence of job processing is: C-E-A-D-B. Both jobs C and E have critical ratios of less than 1.0 and have to be expedited to meet their due dates.
Job C that has the lowest critical ratio has the highest priority and should be scheduled first followed by job E.
Job A is on schedule and jobs B and D have some slack. After Job C is completed, we should re-compute the critical ratios for the remaining four jobs to determine if their priorities have changed.

## Slide 25: Sequencing N Jobs Through Two Machines: Johnson’s Rule
Step 1: List all jobs along with their processing times on the work centers or machines for both processes.
Step 2: Find the jobs with the minimum processing times in both work centers or machines.
Step 3a: If the minimum processing time is in the first process, then place the associated job in the first available place in the sequence. Go to Step 4.
Step 3b: If the minimum processing time is in the second process then place the associated job in the last available place in the sequence. Go to Step 4.
Step 4: Remove assigned jobs from further consideration. Return to Step 1 until job is assigned.

## Slide 26: Example 19.4
A group of five jobs needs to go through a two-machine flow shop. The first operation involves grinding and the second is deburring. Use Johnson’s rule to find the optimum sequence of jobs that will minimize the total completion time for these jobs.

## Slide 27: Example 19.4 (Cont’d)
The total time to complete the five jobs in the two machines is 21.3 hours.
The deburring machine has to wait 2.3 hours for the first job, and 0.9 hours for the completion of job B in the first machine (grinding).

## Slide 28: Why Scheduling Is Complex
Most setup and processing times and job priorities vary frequently, and machines set up times depend on the order of job processing.
In a job shop, the high variety and low volume of jobs that require processing through shared resources requires schedule changes and disruptions are inevitable.
Computerized short-term scheduling, often referred to as finite capacity scheduling (FCS), removes many of the drawbacks of rule-based scheduling.

## Slide 29: Theory of Constraints
Theory of constraints aims to achieve a balanced flow through the manufacturing process.
Identify the constraints (Identify the bottleneck operations or resources).
Exploit the constraints (Plan how to make full use of these limiting resources or operations).
Subordinate all other non-constraining resources to the decisions made in the first two steps.
Elevate the constraints (Find ways to eliminate the constraints that are limiting performance).
If the identified constraint is “broken” then go back to Step 1 to identify the next-highest constraint.

## Slide 30: Scheduling in Service Organizations
Unlike manufacturers who can use inventories to smooth out demand fluctuations, it is not possible to store or inventory services.
The fluctuating demand for services and customization need makes scheduling more difficult.
Services may be difficult to schedule because services are typically labor intensive and often require employees with specialized skills.
Service schedules are constrained by legal requirements and union contracts that dictate the number hours that employees can work in given time period.

## Slide 31: Decision Rules for Workforce Scheduling With Two Consecutive Days Off
Step 1: Determine the daily workforce requirements for the all 7 days of a given week in a table.
Step 2: Highlight the two consecutive days that have the lowest total workforce requirements.
Step 3: Add a row for second employee by subtracting 1 from daily requirements of the previous row.
Step 4: In the new row, highlight the two consecutive days that have the lowest total requirement.
Step 5: Repeat Steps 3 and 4 until all workforce requirements are met.

## Slide 32: Example 19.5
The Chief of Police of Millcreek Township, Jennifer Taylor, wants to construct a workforce schedule for his department’s police officers using a standard 5-day work week with two consecutive days off. Jennifer’s objective is to minimize the total amount of excess capacity. The staffing requirements for a second week of January are given in the table:

## Slide 33: Example 19.5 (Cont’d)

## Slide 34: Example 19.5 (Cont’d)

## Slide 35: Example 19.5 (Cont’d)
Jennifer needs 11 police officers to meet the staffing needs. The final schedule is as shown in the table below. In that table, X represents a working day and O is a day off.

## Slide 36: Supply Chain Scheduling
The ability of individual companies to meet performance measures really depends on the scheduling decisions made by the upstream and downstream partners of their supply chains.
The purpose of supply chain scheduling is to analyze the scheduling problems throughout a supply chain that includes suppliers, manufacturer, distributors, and third-party logistics providers and to coordinate the schedules of all of the supply chain members.
This coordination is accomplished through information sharing and cooperation among members of the supply chain.

## Slide 37: Ethical and Sustainability Issues in Scheduling
Traditional scheduling performance measures ignore the negative impact that manufacturing and transportation operations can have on the environment.
Scheduling decisions made by these companies can play a vital role in improving the energy efficiency their manufacturing operations.
In the service sector, scheduling hospital employees has been problematic.
For many hospital employees, particularly doctors and nurses, balancing their work hours and personal life has been a huge challenge.