## Slide 2: Module E: Learning Curves

## Slide 3: Learning Objectives
Define the concept of learning curves.
Identify the various ways to apply learning curves for operations processes.
Apply various approaches to solving learning curve problems.
Implement learning curves for cost estimation problems.
Discuss the advantages and limitations of learning curves.

## Slide 4: Boeing: Relying on Learning Curves for Cost Analysis and Pricing
It might cost $100 million to build the first model of a new airplane, $80 million to build the second, $64 million to make the fourth, etc.
Plotting these production costs against units of production yields a learning curve that slopes from the upper left to the lower right.
From the start of production at the Everett, Washington plant, it now takes 40 days to push a new 787 out the door.
On the other hand, at the Columbia, South Carolina plant, the learning curve still lags to a 56 day process.

## Slide 5: What Are Learning Curves?
Learning curves show that as the production rate for an item doubles, the processing time per unit of that item decreases by a constant percentage.
The time reduction per repetition will steadily decrease as the number of repetitions or units produced increases.

## Slide 6: Applications of Learning Curves
Although uses of learning curves were known as early as 1885, they were first applied in the aircraft industry in 1936.
In addition to its broad applications in the manufacturing and service sectors, learning curves have been found to be useful in specific areas which include:
  Workforce planning and scheduling
  Cost estimation and budgeting
  Procurement negotiations in supply chains
  New product pricing

## Slide 7: Approaches to Solving Learning Curve Problems (Arithmetic Approach)
The arithmetic approach is the simplest of the three approaches and is based on the assumption that as production doubles, the per unit production time declines by a constant percentage, often referred to as the learning rate.

## Slide 8: The Logarithmic Approach
The logarithmic approach uses the following formula to determine the number of direct labor hours required to produce the nth unit:
Tn = T1 x nb where,
Tn = the time required to produce the nth unit
T1 = the time required to produce the first unit
b = ln (learning rate)/ln (2), where “ln” stands for natural logarithm.

## Slide 9: Example E.1
Trinity Hospital just completed its first kidney transplant, a procedure that took 40 hours. During the month of May the hospital has four more kidney transplants scheduled. Based on other similar procedures that the hospital has conducted, the hospital estimates that it has an 85% learning rate. Estimate the time it will take to complete:
  The third transplant
  The fifth transplant
  The total time required for all five transplants

## Slide 10: Example E.1 (Cont’d)

## Slide 11: Use of Table of Learning Curve Coefficient Values
The third approach to solving learning curve problems is to select learning curve coefficient values from a table and use them in the following formula.
For any given value of the learning rate, and n, the number of repetitions of the task or units produced:
Time required nth repetition or produce the nth unit
Tn = T1 x Unit time coefficient value
Total or cumulative time required to produce n units
Total time = T1 x Total time coefficient value

## Slide 12: Use of Table of Learning Curve Coefficient Values (Cont’d)

## Slide 13: Example E.2
Purple Airlines has ordered 28 small jet aircrafts from Prince Aeronautics, Inc. Prince Aeronautics has estimated that the first aircraft will require 360 days of direct labor to manufacture and assemble. From past experience on the production of similar aircrafts, Prince Aeronautics estimates that the learning rate is 75%. Estimate the number of days of direct labor:
  For the 15th jet aircraft
  For all 28 jet aircrafts
  The average number of days for the 28 jets

## Slide 14: Example E.2 (Cont’d)
Given: T1 = 360 days; Learning rate = 75%
a) Table E.2, for n = 15 and learning rate of 75%,
Unit time coefficient value = 0.325
Number of days required to produce the 15th unit
T15 = 360 x 0.325 = 117 days,
b) Table E.2, for n = 28 and learning rate of 75%,
Total time coefficient value = 10.955
Total time = 360 x 10.955 = 3,943.8 days of labor
c)The average number of days = Total time/ n
= 3,943.8/28
= 140.85 or 141 days

## Slide 15: Considerations for Employing Learning Curves
First, it is important to note that different production features will affect the degree of learning that takes place (i.e., the learning rate).
Second factor to consider is that a company may decide to first conduct work sampling on their production assemblies to examine the various assembly or manufacturing systems and determine where the greatest opportunities for learning, and applying learning curves, are centered.
Finally, it is also important to note that to be the most effective, learning curves should be applied to production lines that have rather than production lines that are still being modified or improved.

## Slide 16: Learning Curves in Cost Estimation
Cost estimation, particularly for labor hours, often assumes a uniform rate at which work is done.
When performing multiple activities, the amount of time necessary to complete the first activity is not significantly different from the time necessary to complete the nth activity.
In software development, it is considered standard practice to estimate each activity cost independently of other related activities with which the programmer is involved.

## Slide 17: Example E.3
The worker must do a total of 15 of these activities to reach the steady state. The time estimated to perform the 15th iteration is 1 hour, and the construction firm knows from past experience the learning rate for this highly repetitive activity is 70%. The cost of labor is $35 an hour. Using this information, calculate:
  a. The estimated time necessary to complete the first activity
  b. The direct total labor cost for 15 iterations of these activities

## Slide 18: Example E.3 (Cont’d)
Given: Learning Rate = 0.70; T15 = 1 hour; Direct labor Cost = $35/hour
b = ln 0.70/ln2 = -0.3567/0.6931 = -0.5146
As, Tn = T1 x nb, we have
T15 = 1 =T1 x (15)-0.5146; Hence, T1= 1 / (15)-0.5146 = 4.03 hours.
Table E-2, for n =15, and a learning rate of 70%,
Total time coefficient value = 6.274
Total time = T1 x 6.274 = 4.03 x 6.274 = 25.28 hours.
For a labor cost of $35/hour, the total labor cost is:
Total labor cost = 25.28 x $35 = $884.80

## Slide 19: Limitations of Learning Curves
Learning rates differ from company to company.
Learning curves provide estimates of actual times.
Times estimates for subsequent repetitions are based on the time to perform the first iteration.
Changes to workers or job design may alter the trajectory of learning curves.
Learning curves have limited use in mass production situations as the improvements are negligible.
If a worker is not motivated or bored by conducting repetitive tasks, then very little learning occurs.
Learning curves are mostly applicable to direct labor and materials.